UDA1380

Speaker AS07104PO-R (no symbol, https://pl.farnell.com/pui-audio/as07104po-r/speaker-0-1-20khz-4-ohm-86dba/dp/4411395?CMP=GRHB-OCTOPART)

Humidity sensor Kitronik 56107 https://resources.kitronik.co.uk/pdf/56107-kitronik-mini-prong-soil-moisture-sensor-datasheet.pdf

Temperature sensor https://app.ultralibrarian.com/details/16911694-103f-11e9-ab3a-0a3560a4cccc/Texas-Instruments/TMP175AIDR)

CODEC
The microcontroller communicates with the codec by I2C first, to set it up, and then by I2S to send the audio data.
For I2C it uses SDA and SCL. For I2S it uses WSI, BCKI and DATAI., since the microcontroller will be the master and the codec will be the slave WSO, BCKO and DATAO are unused because we do not send data back to the microcontroller.
Also we can use either SYSCLK or WSI or both for clock signal of I2S, it depends on the program, so both should be enabled just in case.

Up to 47u: 0603 SMD

680u: 1010 SMD https://eu.mouser.com/ProductDetail/KEMET/A768MS687M1DLAE015?qs=vmHwEFxEFR8dgIyPaI7tmg%3D%3D (cheaper but bigger)
https://eu.mouser.com/ProductDetail/KYOCERA-AVX/APA1010681M016R?qs=Wj%2FVkw3K%252BMDX63EfozKqAA%3D%3D (smaller but more expensive)

 220u: 0609 SMD https://eu.mouser.com/ProductDetail/KEMET/EEV227M016A9HAA?qs=sGAEpiMZZMsh%252B1woXyUXjzIg7W%2Fy3DAncDG5AqJJgMk%3D

Ferrite beads: https://eu.mouser.com/ProductDetail/Wurth-Elektronik/742861160?qs=iRra8H4EogopsH%2FG3w0uIA%3D%3D (audio codec)

https://www.we-online.com/components/products/datasheet/742792662.pdf (for amplifier?)
https://eu.mouser.com/ProductDetail/Wurth-Elektronik/742792656?qs=Wn16VcyqZWoo9n9yWYHrQg%3D%3D

ABOUT GROUND PCB: